## Slide 1: Processor implementation on Altera DE2 Development and Education Board
V. Mitić, M. Petković, D. Todorović 1, Volker Zerbe 2
1 - University of Nis, Faculty of Electronic Engineering; 2 - University of Applied Sciences, Erfurt

## Slide 2: Agenda
Introducing to:
  Hardware
    Altera Developement and Education Boards
    FPGAs
  Software
    Programming tools for FPGAs
    VHDL

## Slide 3: Introduction
Technology
Altera Quartus II
DE2 Development and Education Board

## Slide 4: DE2 Development and Education Board

## Slide 5: Elements of the board used
Elements | Role
Switches SW10 TO SW18 | NUMBER A
Switches SW0 TO SW7 | NUMBER B
Swithes SW8 and SW9 | OPERATION SELECTOR
Pushbuttons KEY0 TO KEY 3 | OPERATION SELECTOR, TRIGGER
LEDs LEDR0 TO REDL8 | RESULT (in binary numeral system)
Displays HEX0 TO HEX2 | RESULT (in decimal numeral system)

## Slide 6: Design, fabrication and code
Processor Block Diagram/Schematic file
Operations symbols
  8bitadder, 8bitsupstract, 8bitand, 8bitor, 8bitnot, 8bitxor, 8bitnand, 8bitnor
Multiplexer symbols
  Multiplexernot, Multiplexer, Multiplexer2, Multiplexerrez
HEXdec symbol
Converter symbol

## Slide 7
Processor Block
Diagram/Schematic file
Input numbers
Operations
Multiplexers
HEXdec
Output LEDs
Input pushbuttons
Input selector switches
Output Displays

## Slide 8: Operations symbols
Symbol name | Role | Number of I/O pins
8bitadder | Addition of two numbers | 8/9
8bitsupstract | Substraction of two numbers | 8/9
8bitand | Logical AND | 8/8
8bitor | Logical OR | 8/8
8bitnot | Logical NOT | 8/8
8bitxor | Logical XOR | 8/8
8bitnand | Logical NAND | 8/8
8bitnor | Logical NOR | 8/8

## Slide 9: Operations symbols
8bitadder Addition is done with the use of two symbols: halfadder and fullader.
Symbol name | Input pins | Output pins
HALFADDER | A,B | SUM,CARRY
FULLADDER | A,B,CARRY_IN | SUM,CARRY

## Slide 10
HALFADDER
FULLADDER

## Slide 11: Multiplexer symbols
Symbol name | Number of input pins | Number of output pins | Number of selector pins
Multiplexernot | 16 | 8 | 2
Multiplexer | 34 | 9 | 4
Multiplexer2 | 32 | 8 | 4
Multiplexerrez | 17 | 9 | 2

## Slide 12: Multiplexernot
There are two 8-bit numbers on the input and two selector pins (SEL0-SEL1)
There is one 8-bit number on the output.
The output number is eaqual to one of the input numbers depending of the selector pins.

## Slide 13: HEXdec symbol
This symbol performs conversion of a binary number, which is at the input, into a decimal number which is displayed on the 7- segment displays.
There are 9 input and 49 output pins.
The conversion from binary to decimal numeral system is implemented using converter symbol.
Representation of a number onto 7-segment display is done with symbols HEX0-HEX9.

## Slide 14: Converter symbol
This symbol is a graphical representation of converter.vhd file that is written in VHDL code.
This symbol does not only convert the number, but also it “determines” the distribution of digits in the decimal number.
There are 9 input pins and 29 output pins.
All commands are executed in a process (named CONVERSION) because they have to be executed sequentially (one by one).

## Slide 15: Results in brief
Aquired knowlage about:
  Elements and posibilities of DE2 Development and Education Board
  Basics of VHDL (via converter.vhd)
  Altera Quartus tools for synthesis and simulation
  FPGAs

## Slide 16: Conclusion
DE2 Developement and Education board advantages
FPGA advantages
VHDL advantages
Implementation: from lab demos to ESA projects

## Slide 17: Thank you for your attention!
Any questions?