Achieved results in year 2011

| Theme | Task | 2011 | Planed for 2011 | Achieved in 2011 | Researcher | Head of research |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Publication Type | Number of publications | Publication Type | Number of publications |  |  |
| 3 | 2. Design of analog-to-digital converters for poly-phase applications | h | M61 | 1 |  |  | D. Mirković | P. Petković |

Report for year 2011

3.2 Design of analog-to-digital converters for poly-phase applications

Analog-to-digital converter (ADC) is the main input block in IMPEG (Integrisani Merač Potrošnje Elektirčne enerGije) solid state power-meter designed in LEDA as ASIC for electric power measuring applications. The first version of IMPEG prototype circuit has been designed and fabricated 2005. This version was meant to be built-in into single-phase power meters (IMPEG1). Figure 3.2.1 shows the block diagram of this circuit. It is obvious that ADC block represents the analog frontend in IMPEG1.

Figure 3.2.1 Block diagram of IMPEG1 circuit

The prime purpose of ADC is to convert instantaneous values of current and voltage to digital domain. Conversion takes place in two separate channels for current and for voltage. The main functional block of ADC’s analog part is ΣΔ modulator [1]. Modulator serves to shape noise which originates from analog-to-digital signal discreatization. Practically, the useful signal (the carrier) of 50Hz is oversampled with 524288 Hz. The modulator suppresses HF noise out of signal base band. One of the design requests is to process up to 22 harmonics, so the signal base band is adopted to be 2kHz. This implies noise rejection to high frequencies while the signal is processed with a low pass frequency (LP) filter. Integrators are used for LP filtering. The order of LP filters depends on the required order of noise shaping defines. Actually, it depends on needed ADC parameters. Signal to noise Ratio (SNR) and SFDR (Spurious Free Dynamic Range) are the most important input parameters in ADC design. They characterize the required resolution in terms of the number of output bits [1]. The requested dynamic range (80dB in current and 60dB for voltage channel) implied the use of the third order filtering in current and second order for voltage channel as Fig. 3.2.1 indicates. However measurements on the prototyped samples have shown that the second order filtering is sufficient for both channels. The nature of ΣΔ modulator is to operate with oversampled high frequency but with few number of output bits. IMPEG1 operates as single bit at output channel. In order to obtain multi-bit output one needs decimation digital filter. It accumulates the output signal with the oversampling frequency and provides wider digital word at the output at lower frequency. This word is a digital representation of instantaneous value of voltage and current, respectively.

The digital data is further fed into the Digital Signal Processing (DSP) block. DSP calculates RMS values of current and voltage, active power, reactive power, apparent power, electric energy, power factor (displacement factor) and frequency. This single-phase version of IMEG chip was prototyped in CMOS 0.35 μm AMI Semiconductor technology.

The next generation of IMPEG solid-state power meters, named IMPEG2, was enhanced to fit for three-phase systems. Besides simultaneous acquisition of currents and voltages for all three phases, it was upgraded with several new features. Some of those are Real Time Clock (RTC), Power On Reset (POR) circuits, embedded 8052 microprocessor unit, embedded drivers for LED display and two UART communication ports. Analog part of ADC was simply tripled for all three phases per channel. Therefore IMPEG2 was designed to have six ΣΔ modulators (three for currents and three for voltages of every phase). However due the digital part of the ADC has been redesign in a quite different manner comparing to IMPEG1. An original solution published in [2] uses the same digital filter for processing of all three phases. This was obtained by using the multiplexing technique for all three current and all three voltages. Moreover, MAC architecture has been used for decimation filters.

The subsequent generation of IMPEG (IMPEG3) has been oriented to low power design and to the reduction of the chip area. MPU has been redesigned as well. The facilities have been enriched with few new features. A built-in temperature sensor has been added together with an appropriate self-calibration technique. The main difference in analogue front-end was to perform multiplexing at ADC input. Therefore a number of potential architectural solutions were published in [3]. All of them considered separated current and voltage channel. This approach was motivated by different dynamic ranges and noise sensitivity. Figure 3.2.2 depicts block diagram of the proposed architecture.

Figure 3.2.2 Block diagram of multiplexed second order ΣΔ modulators

Concept illustrated on Figure 3.2.2 can be expanded to four inputs where the fourth port may be used for zero line current or for an external temperature sensor. The new version of IMPEG that is the subject of this project will be designed to accept eight analog signals. This part of the report considers a new concept for multiplexed analog inputs. It relays on experiences obtained with the previous versions. Therefore, they will be shortly explained before we suggest a new architecture.

Architecture of modulators built-in IMPEG1-3 is CIFB (Cascade of Integrators Feed-Back) [1]. Figure 3.2.3 shows block diagram of the second order ΣΔ modulator with CIFB architecture.

Figure 3.2.3 Block diagram of second order ΣΔ modulator with CIFB architecture

Blocks denoted with I represent DAI (Discrete Analog Integrators) with delay whose Z domain transfer function is given as:

,                                                                       (3.2.1)

where z is complex variable. Input voltage is denoted with Vin, while VI1 and VI2, represent the output of the first and the second integrator, respectively. Output of single-bit quantizer after i-th step is denoted with gi. It can take values from set {1, -1}. The single-bit output of DAC is defined with term giVref, where Vref is the reference voltage. According to calculations given in [4], coefficients of modulators are:

a1 = 1.0, a2= 0.5, af1= 0.301, af2 = 0.24.                                        (3.2.2)

The modulator is realized as Switched Capacitor (SC) circuit. More about architecture and realization of modulator shown on Figure 3.2.3 can be found in [4]. Since signal has to be constantly present on the input of a classic ΣΔ modulator, this architecture is not suitable for multiplexed application. So it is necessary to introduce a new architectural solution for ΣΔ modulator. In other words, classic ΣΔ type of ADC architecture is not favorable in combination with multiplexer on its input. The main problem with classic ΣΔ converter is too long settling time of digital part, i.e. digital filters that cause unacceptable delay between multiplexed channels. Therefore the architecture published in [5] is more suitable for multiplexing. This architecture is known as CIFF (Cascade of Integrators Feed-Forward) [6]. In order to be ready for accepting data from a new channel, ADC has to be reset after every conversion cycle. This implies that reset mast be introduced in ADC system. This kind of oversampling ADCs which contains resettable ΣΔ modulators are usually named charge transfer, single shot or incremental ADC.

Operation of incremental ADC is based on dual-slope ADC modification. The modification concerns the order of integration of input and reference signal. In dual-slope ADC the integration takes place in two separate phases, while in incremental ADC it occurs alternately with clock signal. This property of alternate integration of input and reference signal is provided by using oversampling technique as with classic ΣΔ ADCs. Basically, incremental ADC is a hybrid converter which compromises between dual-slope and classic ΣΔ ADC type of converters. As with dual-slope ADC, the incremental ADC has to have constant value of input signal for whole conversion cycle, as well. It is worth to mention that this was not a case with classic ΣΔ ADC. Because of this fact, SH (Sample and Hold) circuit mast precede the incremental ADC modulator.

Figure 3.2.4 represents CIFF architecture of second order ΣΔ modulator. Obviously, this architecture has only one feedback path from output (Y) to input (X), in contrast to CIFB architecture (Fig. 3.2.3) that has two.

Figure 3.2.4 Block diagram of second order ΣΔ modulator with CIFF architecture

According to Figure 3.2.3, blocks denoted with I represent DAI with Z domain transfer function given in (3.2.1). In Figure 3.2.4 Vin, VI1 and VI2, denotes input voltage and output voltage of the first and the second integrator, respectively. The output voltage of the single-bit DAC, denoted by term giVref, took values (Vref. Constants a1, a2, c1 and b are modulator coefficients.

The modulator operates as follows. Let suppose that the conversion of one input value requires n clock cycles. Each conversion starts from the initial state with VI1[0] = VI2[0] =0V. The subsequent n outputs at the first integrator will take the following values:

(3.2.3)

where Vin[i] and VI1[i] stand for input analog voltage and the output voltage of the first integrator after i clock cycles, respectively while gi denotes state of the quantizer after ith cycle. Similarly, the output of the second integrator will be:

(3.2.4)

where VI2[j] is output voltage of the second integrator after jth clock cycle j=0,...,n. This voltage takes value in range ± Vref.

(3.2.5)

During the conversion SH circuit provides constant analog input signal Vin[j] = Vin0, for j=1,...,n. Therefore its contribution to the total sum in (3.2.4) is:

(3.2.6)

Substitution of (3.2.6) into (3.2.4) and (3.2.5) provides important result given in (3.2.7).

(3.2.7)

The middle term of (3.2.7) represents the difference between analog input and the converted digital signal. Practically, it stands for conversion error that is bounded with ± (1/2)⋅VLSB, where VLSB is the analog voltage equivalent of the least significant bit. Therefore, it is defined as:

(3.2.8)

Resolution of the converter can be expressed as:

(3.2.9)

where, nbit is a number of bits. Assuming n≫1 one gets:

(3.2.10)

For the full dynamic range of the input signal of Vinmax = +Vref – (–Vref) = 2⋅Vref, and for normalized architecture (all modulator’s coefficients equal to one) the resolution is reduced to:

(3.2.11)

Equations (3.2.10) or (3.2.11) allows calculation of the minimum number of clock cycles, n, needed to obtain nbit resolution.

Supposing that the required dynamic range is 96bB it is easy to find that nbit = 96/6 = 16 will met the request. According to (3.2.11) one easily calculates the minimum number of clock cycles to be nmin = 362. This means that the conversion of one channel lasts for 362 clock intervals. According to [6], in order to prevent saturation of integrators it is good practice to adopt Vinmax ∼ 0.67Vref for second order modulator. Consequently this increases the minimum number of clock cycles to nmin = 512. More information about evaluating nmin for higher order modulators can be found in [6].

So far we determined the architecture and operation condition of the modulator. The next step is to define decimation filter that should average nmin bit stream to provide nbit digital output. It is good practice to choose filter to be at least one order higher than the modulator. Therefore this report will consider a third order Sinc filter.

In general, transfer function of the Lth order Sinc filter expressed in z-domain is:

(3.2.12)

where M= fs/fn is the oversampling ration, fn is Nyquist frequency defined as fn = 2⋅BW and BW represents signal base band-width. In the particular case of IMPEG BW = 2048Hz. Realization of the Sinc filter is simplified if M=2K, where K is an integer.

Equation (3.2.12) allows determining the sampling frequency. Actually the algorithm comprises the following steps:

- For given nmin (nmin= 512) and adopted order of the modulator La (La = 2) determine the order of digital Sinc filter L = La + 1 (L= 3).

- Increase nmin until obtain M = nmin/L to be the first larger 2K number. (M= nmin/L=512/3=170.667; the first larger 2K is 256; choose M = 256 and recalculate nmin = L∙M=768).

- Determine sampling frequency as fs=M⋅fn = M⋅(2⋅BW) (fs = 220 Hz ≈ 2 MHz)

After nmin clock cycles filter will provide 16-bit digital word at the output. Therefore, one conversion cycle requires nmin/fs ≈ 732.42μs. The existing ΣΔ ADC in previous IMPEG versions provides digital data three times faster with 4096Hz rate, i.e. at every ∼ 214.14μs. In order to maintain the same data rate towards digital part of the chip, a new three times higher sampling frequency is adopted (fsnew = 3⋅220 Hz ≈ 3.14 MHz). Eventually, the output of the digital filter provides 16-bit wide word after nmin/fsnew =1/4096s ∼ 214.14μs.

Let consider a multiplexed ADC with N input signals (channels) based on architecture from Figure 3.2.4. According to the fact that nmin depends on the required resolution (which was not be the case with classic ΣΔ ADC), the multiplexing with the specified precision is feasible if N⋅nmin clock periods which fit within the available time window. The purpose of this project is to obtain N=4 conversions within the same time window of 214.14μs. This means that the 16-bit output word appears for all four channels with the rate of 4096Hz.Therefore the conversion time should be four times shorter for each channel and consequently, the new sampling frequency has to be N=4 times higher (fsN=N·fs). After nmin clock periods, the obtained output of one channel is buffered, the whole converter (modulator and digital filter) is reset and another channel is fed to the input of ADC. This cycle repeats for all of N input channels. When Nth channel is converted, the buffered digital words are fed to DSP unit in parallel. The algorithm of conversion for N-channel multiplexed, incremental ADC contains the following steps:

- First channel is selected with analog multiplexer.

- With SH circuit selected signal is sampled and held for whole conversion cycle at the ADC’s input.

- After nmin/fsN (1/214 s ≈ 61μs) digital output word is obtained and buffered for the selected channel; ADC is reset; and the subsequent new channel is selected from analog multiplexer to the ADC input.

- Step 3 is repeated N times for all input channels.

- After conversion of N-th channel; N nbit -bit words are red with rate fsN/(nmin⋅N) (fsnewN/(nmin⋅N) = 4096 Hz); the procedure repeats from step 1.

One could conclude that due to the multiplexing a delay of nmin/fsN = 61μs appears between each channel that could reflect on signal phase. Because the signal frequency is 50Hz, i.e. period 20ms, delay is only is about 0.3% of the signal’s period. Therefore the phase error is negligible. Nevertheless it is necessary to examine its influence on overall power and energy calculation. Obviously it is a systematic error that can be eliminated later in the digital part of the chip by the built-in programmable compensation.

So far the stability has not been considered. However it is an important feature of modulators. According to the common practice the stability will be appraised by analyzing the modulator behavior in z-domain. In  convertors noise signal is fed back to the input and consequently it is responsible for stability. Therefore it is of important interest to analyze distributions of poles in Noise Transfer Function (NTF).  According to Figure 3.2.4 the output signal Y is defined with:

(3.2.13)

where e represents noise produced by quantizer, and NTF is Y/e ratio for X→0. Therefore:

(3.2.14)

Obviously the second order filter gives second order NTF. Modulator will be stabile if pair of NTF poles, p1 and p2, are placed inside the unit circle in z-plane. As earlier mentioned, for a second order modulator, it is good practice to limit integrator output voltages on 0.67Vref.

The design task is to determine coefficients values that provide stabile and reliable operation. For adopted M=256, VImax = 0.67Vref and maximum NTF out of band gain of 2, MATLAB® Delta-Sigma Toolbox [7] evaluated NTF to be:

(3.2.15)

The corresponding magnitude of NTF is shown in Figure 3.2.5. Obviously the out of band gain is 6dB (2 times), and on the band edge (∼2kHz) noise is suppressed to –111dB. The slope of the noise shaping is 20dB/dec that corresponds to the second order noise shaping. Figure 3.2.6 depicts zero-pole locus in Z plane.

Figure 3.2.5 NTF magnitude response

NTF complex conjugate poles have values p1/2 = 0.3819 ± j⋅0.3004. Mapping these poles on CIFF architecture, resulted in coefficients defined as:

b = 0.475, c1= 0.598, a1= 2.59, a2 = 2.755.                                 (3.2.16)

The architecture of four channels multiplexed, incremental ADC was verified on, behavioral MATLAB® Simulink model Presented in Figure 3.2.7.

Figure 3.2.6 Z plane NTF zeros/poles locus

Figure 3.2.7 Data flow block diagram of voltage channel ADC

Sampling frequency of modulator is fsN =12MHz (12582912Hz), while with fsN/nmin =16384Hz rate analog multiplexer and SH circuit are clocked and reset of the entire ADC (modulator and digital filters) is performed. ADC is verified in presence of four sinusoidal signals with the same frequency of 50Hz and with amplitudes of 200mV, 100mV, 50mV and 25mV at inputs VinR, VinS, VinT and VinZ, respectively. Phases of VinR, VinS, and VinT are shifted for for 120o while VinZ have the same phase as VinR. Figure 3.2.8 illustrates waveforms of input and the output signals.

Figure 3.2.8 Time waveform of converted (A) and input (B) signals 
of incremental ADC in voltage channel

The best insight into circuit behavior give signal spectrum obtained by FFT analyzes over ADC’s outputs. Figure 3.2.9 illustrates the obtained results. Figure 3.2.9.a presents the complete, single-sided, signal spectrum up to the base band of 2kHz. Figure 2.3.9.b depicts magnified part of the spectra around 50Hz in order to as to clearly verify presence of all four signals. Obviously the obtained result confirms functionality of the proposed multiplexed, incremental, ADC architecture.

It should be mentioned that the current channel has identical architecture. Experience with previously prototyped IMPEG version suggests that the obtained SFDR better than 130dB at behavioral level have good chances to satisfy requested dynamic range of 80dB in current channel after tape-out. The further research will consider other ΣΔ modulator and/or digital filter architectures. It has been shown in [6] that good results can be obtained with simpler digital filter architectures, as well (e.g. cascade of two digital integrators). Therefore, the expectation of better matched ADCs and reduced area comes through. Every, new, architecture should be well examined for design requirements in terms of dynamic range, resolution and noise sensitivity.

a)						      b)

Figure 3.2.9 One side magnitude spectrum of four channel ADC output

a) Full spectrum, logarithmic frequency scale; b) Part of spectrum around 50Hz, linear frequency scale

Literatura 6.1

1. R. Schreier, and G. C. Temes., ”Understanding Delta-Sigma Data Converters”, John Wiley & Sons, Inc., Hoboken, New Jersey, 2005.

2. Marinković, M., „Decimacioni filtri u trofaznom integrisanom meraču potrošnje električne energije“, Magistarska teza, Univerzitet u Nišu, Elektronksi fakultet Niš, 2008.

3. Mirković, D., Petković, P.: Višekanalni ΣΔ A/D konvertor za integrisani merač potrošnje električne energije, Zbornik LIV Konferencije ETRAN, Donji Milanovac, 07.06.  - 11.06., 2010, EL2.5-1-4, ISBN 978-86-80509-65-5

4. Nikolić, M., „Projektovanje lejauta CMOS integrisanih kola sa mešovitim signalima“, Magistarska teza, Univerzitet u Nišu, Elektronksi fakultet Niš, 2006.

5. C. Lyden, C. A. Ugarte, J. Kornblum, and F. M. Yung, “Single shot sigma-delta analog-to-digital converter for multiplexed applications” in Proc. IEEE Custom Integrated Circuit Conf., Santa Clara, CA, May 1-4, 1995, pp. 203-206.

6. J. Márkus, J. Silva, and G. C. Temes, “Theory and applications of incremental delta-sigma converters”, IEEE Trans. Circuit Syst. I, Reg. Papers, vol. 51, no. 4, pp 678-690, Apr. 2004.

7. R. Schreier. (2003) The Delta–Sigma toolbox v6.0 (Delsig). Mathworks, Natick, MA. [Online]. Available: http://www.mathworks.com/matlabcentral/fileexchange/